## Slide 1
European Fuel Cells and Hydrogen
PIERO LUNGHI CONFERENCE 2026
Capri, Naples · 15–17 September 2026
Predictive operation of a hydrogen
refuelling station with scheduled clients
Pol Cardona
Supervisors: Dr. Carlos Ocampo-Martinez, Dr. Maria Serra Prat
Institut de Robòtica i Informàtica Industrial, CSIC-UPC | Automatic Control Department, UPC ·
Barcelona
CSIC/I-LINK2025/ILINK25160
SEAMLESS PID2023-148840OB-I00

## Slide 2
02 / 17
Outline
1
Context
Hydrogen refuelling stations · the research question
2
Proposal
A supervisory hybrid MPC · lexicographic objectives
3
Availability
Cascaded refuelling · the usual premise · patterns ·
the objective
4
Bookings
How a booking enters the model, tank by tank
5
Results
A preliminary six-hour case, three booked clients
6
Conclusions
What this paper answers · what remains

## Slide 3
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
03 / 17
Hydrogen Refuelling Stations (HRSs)
Main characteristics: flexible in sourcing, complex in preparation
1
FLEXIBILITY
Hydrogen
sourcing
on site
off site
1
Hydrogen sourcing
produced on site, or delivered
Electrolyser
on site
Station storage
pressurised
Tube trailer
off site
Which source, and when, is a decision.
2
FLEXIBILITY
Electrical
energy
sourcing
renewables
storage
grid
market
2
Electrical energy sourcing
one bus, several sources, two loads
Renewables
PV, wind
Storage
battery
Grid
import, export
Market
prices, services
ELECTRICAL BUS
Electrolyser
production
Compressors
preparation
Production and compression are the loads.
3
COMPLEXITY
Pressurised
storage and
compression
several
pressure levels
compressors
3
Pressurised storage and compression
lifted in stages to the vehicle standard
low
C
medium
C
high
Vehicle
350 or 700 bar
Which tank to fill, and when, is a decision.
4
COMPLEXITY
Cascaded
refuelling
tanks in
sequence
filling and
refuelling
4
Cascaded dispensing
tanks opened in order, no compressor
1st
2nd
3rd
Dispenser
gradient-driven
Vehicle
pressure rises stepwise
Order matters, in filling and in refuelling.
Source: which, when?
Compress: which tank, when?
Hydrogen needs preparation before delivery: pressure,
order, timing.

## Slide 4
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
03 / 17
Hydrogen Refuelling Stations (HRSs)
Hydrogen sourcing
1
FLEXIBILITY
Hydrogen
sourcing
on site
off site
1
Hydrogen sourcing
produced on site, or delivered
Electrolyser
on site
Station storage
pressurised
Tube trailer
off site
Which source, and when, is a decision.
2
FLEXIBILITY
Electrical
energy
sourcing
renewables
storage
grid
market
2
Electrical energy sourcing
one bus, several sources, two loads
Renewables
PV, wind
Storage
battery
Grid
import, export
Market
prices, services
ELECTRICAL BUS
Electrolyser
production
Compressors
preparation
Production and compression are the loads.
3
COMPLEXITY
Pressurised
storage and
compression
several
pressure levels
compressors
3
Pressurised storage and compression
lifted in stages to the vehicle standard
low
C
medium
C
high
Vehicle
350 or 700 bar
Which tank to fill, and when, is a decision.
4
COMPLEXITY
Cascaded
refuelling
tanks in
sequence
filling and
refuelling
4
Cascaded dispensing
tanks opened in order, no compressor
1st
2nd
3rd
Dispenser
gradient-driven
Vehicle
pressure rises stepwise
Order matters, in filling and in refuelling.
Source: which, when?
Compress: which tank, when?
Hydrogen needs preparation before delivery: pressure,
order, timing.

## Slide 5
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
03 / 17
Hydrogen Refuelling Stations (HRSs)
Electrical energy sourcing
1
FLEXIBILITY
Hydrogen
sourcing
on site
off site
1
Hydrogen sourcing
produced on site, or delivered
Electrolyser
on site
Station storage
pressurised
Tube trailer
off site
Which source, and when, is a decision.
2
FLEXIBILITY
Electrical
energy
sourcing
renewables
storage
grid
market
2
Electrical energy sourcing
one bus, several sources, two loads
Renewables
PV, wind
Storage
battery
Grid
import, export
Market
prices, services
ELECTRICAL BUS
Electrolyser
production
Compressors
preparation
Production and compression are the loads.
3
COMPLEXITY
Pressurised
storage and
compression
several
pressure levels
compressors
3
Pressurised storage and compression
lifted in stages to the vehicle standard
low
C
medium
C
high
Vehicle
350 or 700 bar
Which tank to fill, and when, is a decision.
4
COMPLEXITY
Cascaded
refuelling
tanks in
sequence
filling and
refuelling
4
Cascaded dispensing
tanks opened in order, no compressor
1st
2nd
3rd
Dispenser
gradient-driven
Vehicle
pressure rises stepwise
Order matters, in filling and in refuelling.
Source: which, when?
Compress: which tank, when?
Hydrogen needs preparation before delivery: pressure,
order, timing.

## Slide 6
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
03 / 17
Hydrogen Refuelling Stations (HRSs)
Pressurised storage and compression
1
FLEXIBILITY
Hydrogen
sourcing
on site
off site
1
Hydrogen sourcing
produced on site, or delivered
Electrolyser
on site
Station storage
pressurised
Tube trailer
off site
Which source, and when, is a decision.
2
FLEXIBILITY
Electrical
energy
sourcing
renewables
storage
grid
market
2
Electrical energy sourcing
one bus, several sources, two loads
Renewables
PV, wind
Storage
battery
Grid
import, export
Market
prices, services
ELECTRICAL BUS
Electrolyser
production
Compressors
preparation
Production and compression are the loads.
3
COMPLEXITY
Pressurised
storage and
compression
several
pressure levels
compressors
3
Pressurised storage and compression
lifted in stages to the vehicle standard
low
C
medium
C
high
Vehicle
350 or 700 bar
Which tank to fill, and when, is a decision.
4
COMPLEXITY
Cascaded
refuelling
tanks in
sequence
filling and
refuelling
4
Cascaded dispensing
tanks opened in order, no compressor
1st
2nd
3rd
Dispenser
gradient-driven
Vehicle
pressure rises stepwise
Order matters, in filling and in refuelling.
Source: which, when?
Compress: which tank, when?
Hydrogen needs preparation before delivery: pressure,
order, timing.

## Slide 7
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
03 / 17
Hydrogen Refuelling Stations (HRSs)
Cascaded dispensing
1
FLEXIBILITY
Hydrogen
sourcing
on site
off site
1
Hydrogen sourcing
produced on site, or delivered
Electrolyser
on site
Station storage
pressurised
Tube trailer
off site
Which source, and when, is a decision.
2
FLEXIBILITY
Electrical
energy
sourcing
renewables
storage
grid
market
2
Electrical energy sourcing
one bus, several sources, two loads
Renewables
PV, wind
Storage
battery
Grid
import, export
Market
prices, services
ELECTRICAL BUS
Electrolyser
production
Compressors
preparation
Production and compression are the loads.
3
COMPLEXITY
Pressurised
storage and
compression
several
pressure levels
compressors
3
Pressurised storage and compression
lifted in stages to the vehicle standard
low
C
medium
C
high
Vehicle
350 or 700 bar
Which tank to fill, and when, is a decision.
4
COMPLEXITY
Cascaded
dispensing
tanks in
sequence
filling and
refuelling
4
Cascaded refuelling
tanks opened in order, no compressor
1st
2nd
3rd
Dispenser
gradient-driven
Vehicle
pressure rises stepwise
Order matters, in filling and in refuelling.
Source: which, when?
Compress: which tank, when?
Hydrogen needs preparation before delivery: pressure,
order, timing.

## Slide 8
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
03 / 17
Hydrogen Refuelling Stations (HRSs)
The product needs preparation
1
FLEXIBILITY
Hydrogen
sourcing
on site
off site
1
Hydrogen sourcing
produced on site, or delivered
Electrolyser
on site
Station storage
pressurised
Tube trailer
off site
Which source, and when, is a decision.
2
FLEXIBILITY
Electrical
energy
sourcing
renewables
storage
grid
market
2
Electrical energy sourcing
one bus, several sources, two loads
Renewables
PV, wind
Storage
battery
Grid
import, export
Market
prices, services
ELECTRICAL BUS
Electrolyser
production
Compressors
preparation
Production and compression are the loads.
3
COMPLEXITY
Pressurised
storage and
compression
several
pressure levels
compressors
3
Pressurised storage and compression
lifted in stages to the vehicle standard
low
C
medium
C
high
Vehicle
350 or 700 bar
Which tank to fill, and when, is a decision.
4
COMPLEXITY
Cascaded
refuelling
tanks in
sequence
filling and
refuelling
4
Cascaded dispensing
tanks opened in order, no compressor
1st
2nd
3rd
Dispenser
gradient-driven
Vehicle
pressure rises stepwise
Order matters, in filling and in refuelling.
Source: which, when?
Compress: which tank, when?
Hydrogen needs preparation before delivery: pressure,
order, timing.

## Slide 9
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
04 / 17
RESEARCH QUESTION
Can integrating client demand into the operation of the station bring
quantifiable gains in energy efficiency and demand satisfaction?
FIRST STEP
Can the controller commit to a booked client in
advance and still plan freely?

## Slide 10
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
05 / 17
The proposed approach
A request arrives
CLIENT REQUEST
Booking,
bounded lead
time
requested time slot
mass on board
mass asked
SUPERVISORY
CONTROLLER
Lexicographic hybrid
MPC
Δt = 10 min · 72-step horizon
· MLD model of the station
4 objectives, strict
priority
ANSWER
Feasible or not
Accept
a plan exists; the
slot is committed
Reject
no feasible plan
ROLLING PLAN
Hydrogen
sourcing and
compression
source: when, how
much
compress: when,
into which tank

## Slide 11
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
05 / 17
The proposed approach
Feasible or not
CLIENT REQUEST
Booking,
bounded lead
time
requested time slot
mass on board
mass asked
SUPERVISORY
CONTROLLER
Lexicographic hybrid
MPC
Δt = 10 min · 72-step horizon
· MLD model of the station
4 objectives, strict
priority
ANSWER
Feasible or not
Accept
a plan exists; the
slot is committed
Reject
no feasible plan
ROLLING PLAN
Hydrogen
sourcing and
compression
source: when, how
much
compress: when,
into which tank

## Slide 12
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
05 / 17
The proposed approach
A rolling plan
CLIENT REQUEST
Booking,
bounded lead
time
requested time slot
mass on board
mass asked
SUPERVISORY
CONTROLLER
Lexicographic hybrid
MPC
Δt = 10 min · 72-step horizon
· MLD model of the station
4 objectives, strict
priority
ANSWER
Feasible or not
Accept
a plan exists; the
slot is committed
Reject
no feasible plan
ROLLING PLAN
Hydrogen
sourcing and
compression
source: when, how
much
compress: when,
into which tank

## Slide 13
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
06 / 17
Lexicographic Control Objectives
Four objectives, strict priority
1
Hydrogen availability
Ready for unannounced arrivals
2
Grid import
Compression follows the PV
3
Off-site H₂ purchase
Trailer deliveries
4
Surplus H₂ sale
Monetise last
Lexicographic: strict priority, no weights
Service to booked clients: hard constraint
Bookings are guaranteed by the model, tank by tank.
Grid import leads; availability keeps idle hours open to
short-lead requests.

## Slide 14
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
06 / 17
Lexicographic Control Objectives
Bookings enter as constraints
1
Hydrogen availability
Ready for unannounced arrivals
2
Grid import
Compression follows the PV
3
Off-site H₂ purchase
Trailer deliveries
4
Surplus H₂ sale
Monetise last
Lexicographic: strict priority, no weights
Service to booked clients: hard constraint
Bookings are guaranteed by the model, tank by tank.
Grid import leads; availability keeps idle hours open to
short-lead requests.

## Slide 15
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
06 / 17
Lexicographic Control Objectives
Grid first, availability second
2
Hydrogen availability
Ready for unannounced arrivals
1
Grid import
Compression follows the PV
3
Off-site H₂ purchase
Trailer deliveries
4
Surplus H₂ sale
Monetise last
Lexicographic: strict priority, no weights
Service to booked clients: hard constraint
Bookings are guaranteed by the model, tank by tank.
Grid import leads; availability keeps idle hours open to
short-lead requests.

## Slide 16
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
07 / 17
Cascaded refuelling
Flow follows the pressure gradient
300
bar
Tank A
480
bar
Tank B
⟶
arrival
100
bar
Vehicle
1
Open A: flow to
P
eq,1
, A gives
Δm
A
2
No gradient: A cannot push more, whatever it still
holds
3
Open B: flow to 350 bar, B delivers
Δm
B
4
Order matters:
B → A
stalls at B's equilibrium
Delivered mass =
Δm
A
+ Δm
B
, set by pressures
and volumes, not by stored mass.

## Slide 17
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
07 / 17
Cascaded refuelling
Flow follows the pressure gradient
230
bar
Tank A
480
bar
Tank B
⟶
A → vehicle
230
bar
Vehicle
1
Open A: flow to
P
eq,1
, A gives
Δm
A
2
No gradient: A cannot push more, whatever it still
holds
3
Open B: flow to 350 bar, B delivers
Δm
B
4
Order matters:
B → A
stalls at B's equilibrium
Delivered mass =
Δm
A
+ Δm
B
, set by pressures
and volumes, not by stored mass.

## Slide 18
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
07 / 17
Cascaded refuelling
Flow follows the pressure gradient
230
bar
Tank A
480
bar
Tank B
⟶
no gradient
230
bar
Vehicle
1
Open A: flow to
P
eq,1
, A gives
Δm
A
2
No gradient: A cannot push more, whatever it still
holds
3
Open B: flow to 350 bar, B delivers
Δm
B
4
Order matters:
B → A
stalls at B's equilibrium
Delivered mass =
Δm
A
+ Δm
B
, set by pressures
and volumes, not by stored mass.

## Slide 19
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
07 / 17
Cascaded refuelling
Flow follows the pressure gradient
230
bar
Tank A
350
bar
Tank B
⟶
B → vehicle
350
bar
Vehicle
1
Open A: flow to
P
eq,1
, A gives
Δm
A
2
No gradient: A cannot push more, whatever it still
holds
3
Open B: flow to 350 bar, B delivers
Δm
B
4
Order matters:
B → A
stalls at B's equilibrium
Delivered mass =
Δm
A
+ Δm
B
, set by pressures
and volumes, not by stored mass.

## Slide 20
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
07 / 17
Cascaded refuelling
Flow follows the pressure gradient
230
bar
Tank A
350
bar
Tank B
⟶
done
350
bar
Vehicle
1
Open A: flow to
P
eq,1
, A gives
Δm
A
2
No gradient: A cannot push more, whatever it still
holds
3
Open B: flow to 350 bar, B delivers
Δm
B
4
Order matters:
B → A
stalls at B's equilibrium
Delivered mass =
Δm
A
+ Δm
B
, set by pressures
and volumes, not by stored mass.

## Slide 21
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
08 / 17
The usual premise
The station as one tank
AVAILABILITY, IN THE LITERATURE
Σ m
the station as one tank
Σ m
tanks
≥ m
demand
enough mass in store, the
fill can be served
Rule-based
fill fast, in a fixed order
Optimisation-
based
balance on the total mass,
lumped demand
40 kg
four tanks at 330 bar, request 16
kg
one tank: 40 ≥ 16, serve
cascade: no source above 350 bar, fill fails
22 kg
two tanks at 400 and 500 bar,
request 16 kg
one tank: less in store
cascade: 400 → 500 bar, fill completes
Availability is a property of the stored mass AND pressure distribution. The station is not one tank.

## Slide 22
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
08 / 17
The usual premise
More mass, and the fill fails
AVAILABILITY, IN THE LITERATURE
Σ m
the station as one tank
Σ m
tanks
≥ m
demand
enough mass in store, the
fill can be served
Rule-based
fill fast, in a fixed order
Optimisation-
based
balance on the total mass,
lumped demand
40 kg
four tanks at 330 bar, request 16
kg
one tank: 40 ≥ 16, serve
cascade: no source above 350 bar, fill fails
22 kg
two tanks at 400 and 500 bar,
request 16 kg
one tank: less in store
cascade: 400 → 500 bar, fill completes
Availability is a property of the stored mass AND pressure distribution. The station is not one tank.

## Slide 23
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
08 / 17
The usual premise
Less mass, and the fill completes
AVAILABILITY, IN THE LITERATURE
Σ m
the station as one tank
Σ m
tanks
≥ m
demand
enough mass in store, the
fill can be served
Rule-based
fill fast, in a fixed order
Optimisation-
based
balance on the total mass,
lumped demand
40 kg
four tanks at 330 bar, request 16
kg
one tank: 40 ≥ 16, serve
cascade: no source above 350 bar, fill fails
22 kg
two tanks at 400 and 500 bar,
request 16 kg
one tank: less in store
cascade: 400 → 500 bar, fill completes
Availability is a property of the stored mass AND pressure distribution. The station is not one tank.

## Slide 24
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
08 / 17
The usual premise
Availability is not a mass
AVAILABILITY, IN THE LITERATURE
Σ m
the station as one tank
Σ m
tanks
≥ m
demand
enough mass in store, the
fill can be served
Rule-based
fill fast, in a fixed order
Optimisation-
based
balance on the total mass,
lumped demand
40 kg
four tanks at 330 bar, request 16
kg
one tank: 40 ≥ 16, serve
cascade: no source above 350 bar, fill fails
22 kg
two tanks at 400 and 500 bar,
request 16 kg
one tank: less in store
cascade: 400 → 500 bar, fill completes
Availability is a property of the stored mass AND pressure distribution. The station is not one tank.

## Slide 25
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
09 / 17
Refuelling patterns as a modelling strategy
An ordered sequence of sources
1
Pattern =
ordered
sequence of sources
1
A pattern is an
ordered
sequence of sources
A
B
Vehicle · 350 bar
order matters:
B → A stalls at B's equilibrium
2
Step ends at
350 bar
or at
equalisation
2
A
step
opens one source and ends at the first of two events
300 bar
A
⟶
100 → 230 bar
Vehicle
✓ vehicle reaches 350 bar
= P
A
equalises with P
veh
3
Length ≤
2 steps
, repeats pruned →
36 candidates
3
Length capped at
2 steps
; repeats pruned
1 step
A
6
2 steps
A
B
30
3 steps
A
B
C
0
A
A
≡ A
no gradient left
A
B
B
≡ A → B
A
B
A
✕
A already equalised
4
Available mass per pattern,
linear
in tank masses
4
Available mass of a pattern, in one algebraic step
Pattern T3₂
430 bar
→ T4
720 bar
· vehicle at 100 bar asks 16 kg
Δm
(1)
8.0 kg
Δm
(2)
9.5 kg
request 16 kg ▸
m
av
= Δm
(1)
+ Δm
(2)
=
17.5 kg
≥ 16 kg → feasible
INPUTS PER CLIENT
vehicle tank volume
mass on board at arrival
Previous work · Applied Energy 2025
Which patterns are feasible depends on every tank pressure and on the client. Feasible patterns share tanks.

## Slide 26
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
09 / 17
Refuelling patterns as a modelling strategy
What one step does
1
Pattern =
ordered
sequence of sources
1
A pattern is an
ordered
sequence of sources
A
B
Vehicle · 350 bar
order matters:
B → A stalls at B's equilibrium
2
Step ends at
350 bar
or at
equalisation
2
A
step
opens one source and ends at the first of two events
300 bar
A
⟶
100 → 230 bar
Vehicle
✓ vehicle reaches 350 bar
= P
A
equalises with P
veh
3
Length ≤
2 steps
, repeats pruned →
36 candidates
3
Length capped at
2 steps
; repeats pruned
1 step
A
6
2 steps
A
B
30
3 steps
A
B
C
0
A
A
≡ A
no gradient left
A
B
B
≡ A → B
A
B
A
✕
A already equalised
4
Available mass per pattern,
linear
in tank masses
4
Available mass of a pattern, in one algebraic step
Pattern T3₂
430 bar
→ T4
720 bar
· vehicle at 100 bar asks 16 kg
Δm
(1)
8.0 kg
Δm
(2)
9.5 kg
request 16 kg ▸
m
av
= Δm
(1)
+ Δm
(2)
=
17.5 kg
≥ 16 kg → feasible
INPUTS PER CLIENT
vehicle tank volume
mass on board at arrival
Previous work · Applied Energy 2025
Which patterns are feasible depends on every tank pressure and on the client. Feasible patterns share tanks.

## Slide 27
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
09 / 17
Refuelling patterns as a modelling strategy
At most two steps: 36 candidates
1
Pattern =
ordered
sequence of sources
1
A pattern is an
ordered
sequence of sources
A
B
Vehicle · 350 bar
order matters:
B → A stalls at B's equilibrium
2
Step ends at
350 bar
or at
equalisation
2
A
step
opens one source and ends at the first of two events
300 bar
A
⟶
100 → 230 bar
Vehicle
✓ vehicle reaches 350 bar
= P
A
equalises with P
veh
3
Length ≤
2 steps
, repeats pruned →
36 candidates
3
Length capped at
2 steps
; repeats pruned
1 step
A
6
2 steps
A
B
30
3 steps
A
B
C
0
A
A
≡ A
no gradient left
A
B
B
≡ A → B
A
B
A
✕
A already equalised
4
Available mass per pattern,
linear
in tank masses
4
Available mass of a pattern, in one algebraic step
Pattern T3₂
430 bar
→ T4
720 bar
· vehicle at 100 bar asks 16 kg
Δm
(1)
8.0 kg
Δm
(2)
9.5 kg
request 16 kg ▸
m
av
= Δm
(1)
+ Δm
(2)
=
17.5 kg
≥ 16 kg → feasible
INPUTS PER CLIENT
vehicle tank volume
mass on board at arrival
Previous work · Applied Energy 2025
Which patterns are feasible depends on every tank pressure and on the client. Feasible patterns share tanks.

## Slide 28
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
09 / 17
Refuelling patterns as a modelling strategy
Available mass per pattern
1
Pattern =
ordered
sequence of sources
1
A pattern is an
ordered
sequence of sources
A
B
Vehicle · 350 bar
order matters:
B → A stalls at B's equilibrium
2
Step ends at
350 bar
or at
equalisation
2
A
step
opens one source and ends at the first of two events
300 bar
A
⟶
100 → 230 bar
Vehicle
✓ vehicle reaches 350 bar
= P
A
equalises with P
veh
3
Length ≤
2 steps
, repeats pruned →
36 candidates
3
Length capped at
2 steps
; repeats pruned
1 step
A
6
2 steps
A
B
30
3 steps
A
B
C
0
A
A
≡ A
no gradient left
A
B
B
≡ A → B
A
B
A
✕
A already equalised
4
Available mass per pattern,
linear
in tank masses
4
Available mass of a pattern, in one algebraic step
Pattern T3₂
430 bar
→ T4
720 bar
, vehicle at 100 bar asks 16 kg
Δm
(1)
8.0 kg
Δm
(2)
9.5 kg
request 16 kg ▸
m
av
= Δm
(1)
+ Δm
(2)
=
17.5 kg
≥ 16 kg → feasible
INPUTS PER CLIENT
vehicle tank volume
mass on board at arrival
Previous work · Applied Energy 2025
Which patterns are feasible depends on every tank pressure and on the client. Feasible patterns share tanks.

## Slide 29
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
09 / 17
Refuelling patterns as a modelling strategy
Feasible patterns share tanks
1
Pattern =
ordered
sequence of sources
1
A pattern is an
ordered
sequence of sources
A
B
Vehicle · 350 bar
order matters:
B → A stalls at B's equilibrium
2
Step ends at
350 bar
or at
equalisation
2
A
step
opens one source and ends at the first of two events
300 bar
A
⟶
100 → 230 bar
Vehicle
✓ vehicle reaches 350 bar
= P
A
equalises with P
veh
3
Length ≤
2 steps
, repeats pruned →
36 candidates
3
Length capped at
2 steps
; repeats pruned
1 step
A
6
2 steps
A
B
30
3 steps
A
B
C
0
A
A
≡ A
no gradient left
A
B
B
≡ A → B
A
B
A
✕
A already equalised
4
Available mass per pattern,
linear
in tank masses
4
Available mass of a pattern, in one algebraic step
Pattern T3₂
430 bar
→ T4
720 bar
· vehicle at 100 bar asks 16 kg
Δm
(1)
8.0 kg
Δm
(2)
9.5 kg
request 16 kg ▸
m
av
= Δm
(1)
+ Δm
(2)
=
17.5 kg
≥ 16 kg → feasible
INPUTS PER CLIENT
vehicle tank volume
mass on board at arrival
Previous work · Applied Energy 2025

## Slide 30
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
10 / 17
The availability objective
Built online, from what each pattern can extract
1
INPUT
Hypothetical
client
mass on arrival
hydrogen
demand
1
A hypothetical client
the one the station must stay ready for
mass on arrival
vehicle
asks 16 kg
ALONG THE HORIZON
both are parameters: they can
change with the time of day
Not a booked client. The objective is written for whoever might arrive.
2
MODEL
Available
mass per
pattern
closed form
linear in tank
masses
2
Available mass per pattern
closed form, linear in the tank masses
A · 300 bar
B · 480 bar
vehicle
what this pattern can extract
m
av
= 17.5 kg
from A · 8.0 kg
from B · 9.5 kg
one expression per pattern, evaluated next to the dynamics at every step. No
extra states.
The solver sees what each pattern can extract, not what the tanks
hold.
3
THRESHOLD
Feasibility
available mass
≥ demand
per pattern
3
Feasibility
a threshold on the available mass, per pattern
demand 16 kg ▸
T3₂ → T4
✓
T3₄ → T4
✓
T4
✗
Feasible: the pattern delivers at least the demand. The set changes
with every tank pressure.
4
ONGOING
Availability
disjoint count
≥ target
4
Availability
count the disjoint feasible patterns against a target
ONGOING WORK
FEASIBLE PATTERNS
T3₂ → T4
T3₄ → T4
T3₁ → T3₃
two share T4: only one of them can count
DISJOINT
2
≥
TARGET
2
⇔
AVAILABLE
✓
The target is time-varying: raise it at rush hours, relax it at night.
Feasible: per pattern, per client
Available: disjoint count ≥ target
Availability is a quantity the solver
optimises, not a stored mass. All of it can
vary in time.

## Slide 31
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
10 / 17
The availability objective
Who must the station stay ready for?
1
INPUT
Hypothetical
client
mass on arrival
hydrogen
demand
1
A hypothetical client
the one the station must stay ready for
mass on arrival
vehicle
asks 16 kg
ALONG THE HORIZON
both are parameters: they can
change with the time of day
Not a booked client. The objective is written for whoever might arrive.
2
MODEL
Available
mass per
pattern
closed form
linear in tank
masses
2
Available mass per pattern
closed form, linear in the tank masses
A · 300 bar
B · 480 bar
vehicle
what this pattern can extract
m
av
= 17.5 kg
from A · 8.0 kg
from B · 9.5 kg
one expression per pattern, evaluated next to the dynamics at every step. No
extra states.
The solver sees what each pattern can extract, not what the tanks
hold.
3
THRESHOLD
Feasibility
available mass
≥ demand
per pattern
3
Feasibility
a threshold on the available mass, per pattern
demand 16 kg ▸
T3₂ → T4
✓
T3₄ → T4
✓
T4
✗
Feasible: the pattern delivers at least the demand. The set changes
with every tank pressure.
4
ONGOING
Availability
disjoint count
≥ target
4
Availability
count the disjoint feasible patterns against a target
ONGOING WORK
FEASIBLE PATTERNS
T3₂ → T4
T3₄ → T4
T3₁ → T3₃
two share T4: only one of them can count
DISJOINT
2
≥
TARGET
2
⇔
AVAILABLE
✓
The target is time-varying: raise it at rush hours, relax it at night.
Feasible: per pattern, per client
Available: disjoint count ≥ target
Availability is a quantity the solver
optimises, not a stored mass. All of it can
vary in time.

## Slide 32
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
10 / 17
The availability objective
What can each pattern extract for that client?
1
INPUT
Hypothetical
client
mass on arrival
hydrogen
demand
1
A hypothetical client
the one the station must stay ready for
mass on arrival
vehicle
asks 16 kg
ALONG THE HORIZON
both are parameters: they can
change with the time of day
Not a booked client. The objective is written for whoever might arrive.
2
MODEL
Available
mass per
pattern
closed form
linear in tank
masses
2
Available mass per pattern
closed form, linear in the tank masses
A · 300 bar
B · 480 bar
vehicle
what this pattern can extract
m
av
= 17.5 kg
from A · 8.0 kg
from B · 9.5 kg
one expression per pattern, evaluated next to the dynamics at every step. No
extra states.
The solver sees what each pattern can extract, not what the tanks
hold.
3
THRESHOLD
Feasibility
available mass
≥ demand
per pattern
3
Feasibility
a threshold on the available mass, per pattern
demand 16 kg ▸
T3₂ → T4
✓
T3₄ → T4
✓
T4
✗
Feasible: the pattern delivers at least the demand. The set changes
with every tank pressure.
4
ONGOING
Availability
disjoint count
≥ target
4
Availability
count the disjoint feasible patterns against a target
ONGOING WORK
FEASIBLE PATTERNS
T3₂ → T4
T3₄ → T4
T3₁ → T3₃
two share T4: only one of them can count
DISJOINT
2
≥
TARGET
2
⇔
AVAILABLE
✓
The target is time-varying: raise it at rush hours, relax it at night.
Feasible: per pattern, per client
Available: disjoint count ≥ target
Availability is a quantity the solver
optimises, not a stored mass. All of it can
vary in time.

## Slide 33
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
10 / 17
The availability objective
Which patterns are feasible?
1
INPUT
Hypothetical
client
mass on arrival
hydrogen
demand
1
A hypothetical client
the one the station must stay ready for
mass on arrival
vehicle
asks 16 kg
ALONG THE HORIZON
both are parameters: they can
change with the time of day
Not a booked client. The objective is written for whoever might arrive.
2
MODEL
Available
mass per
pattern
closed form
linear in tank
masses
2
Available mass per pattern
closed form, linear in the tank masses
A · 300 bar
B · 480 bar
vehicle
what this pattern can extract
m
av
= 17.5 kg
from A · 8.0 kg
from B · 9.5 kg
one expression per pattern, evaluated next to the dynamics at every step. No
extra states.
The solver sees what each pattern can extract, not what the tanks
hold.
3
THRESHOLD
Feasibility
available mass
≥ demand
per pattern
3
Feasibility
a threshold on the available mass, per pattern
demand 16 kg ▸
T3₂ → T4
✓
T3₄ → T4
✓
T4
✗
Feasible: the pattern delivers at least the demand. The set changes
with every tank pressure.
4
ONGOING
Availability
disjoint count
≥ target
4
Availability
count the disjoint feasible patterns against a target
ONGOING WORK
FEASIBLE PATTERNS
T3₂ → T4
T3₄ → T4
T3₁ → T3₃
two share T4: only one of them can count
DISJOINT
2
≥
TARGET
2
⇔
AVAILABLE
✓
The target is time-varying: raise it at rush hours, relax it at night.
Feasible: per pattern, per client
Available: disjoint count ≥ target
Availability is a quantity the solver
optimises, not a stored mass. All of it can
vary in time.

## Slide 34
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
10 / 17
The availability objective
How many, without sharing tanks?
1
INPUT
Hypothetical
client
mass on arrival
hydrogen
demand
1
A hypothetical client
the one the station must stay ready for
mass on arrival
vehicle
asks 16 kg
ALONG THE HORIZON
both are parameters: they can
change with the time of day
Not a booked client. The objective is written for whoever might arrive.
2
MODEL
Available
mass per
pattern
closed form
linear in tank
masses
2
Available mass per pattern
closed form, linear in the tank masses
A · 300 bar
B · 480 bar
vehicle
what this pattern can extract
m
av
= 17.5 kg
from A · 8.0 kg
from B · 9.5 kg
one expression per pattern, evaluated next to the dynamics at every step. No
extra states.
The solver sees what each pattern can extract, not what the tanks
hold.
3
THRESHOLD
Feasibility
available mass
≥ demand
per pattern
3
Feasibility
a threshold on the available mass, per pattern
demand 16 kg ▸
T3₂ → T4
✓
T3₄ → T4
✓
T4
✗
Feasible: the pattern delivers at least the demand. The set changes
with every tank pressure.
4
ONGOING
Availability
disjoint count
≥ target
4
Availability
count the disjoint feasible patterns against a target
ONGOING WORK
FEASIBLE PATTERNS
T3₂ → T4
T3₄ → T4
T3₁ → T3₃
two share T4: only one of them can count
DISJOINT
2
≥
TARGET
2
⇔
AVAILABLE
✓
The target is time-varying: raise it at rush hours, relax it at night.
Feasible: per pattern, per client
Available: disjoint count ≥ target
Availability is a quantity the solver
optimises, not a stored mass. All of it can
vary in time.

## Slide 35
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
10 / 17
The availability objective
Not a stored mass: a quantity to optimise
1
INPUT
Hypothetical
client
mass on arrival
hydrogen
demand
1
A hypothetical client
the one the station must stay ready for
mass on arrival
vehicle
asks 16 kg
ALONG THE HORIZON
both are parameters: they can
change with the time of day
Not a booked client. The objective is written for whoever might arrive.
2
MODEL
Available
mass per
pattern
closed form
linear in tank
masses
2
Available mass per pattern
closed form, linear in the tank masses
A · 300 bar
B · 480 bar
vehicle
what this pattern can extract
m
av
= 17.5 kg
from A · 8.0 kg
from B · 9.5 kg
one expression per pattern, evaluated next to the dynamics at every step. No
extra states.
The solver sees what each pattern can extract, not what the tanks
hold.
3
THRESHOLD
Feasibility
available mass
≥ demand
per pattern
3
Feasibility
a threshold on the available mass, per pattern
demand 16 kg ▸
T3₂ → T4
✓
T3₄ → T4
✓
T4
✗
Feasible: the pattern delivers at least the demand. The set changes
with every tank pressure.
4
ONGOING
Availability
disjoint count
≥ target
4
Availability
count the disjoint feasible patterns against a target
ONGOING WORK
FEASIBLE PATTERNS
T3₂ → T4
T3₄ → T4
T3₁ → T3₃
two share T4: only one of them can count
DISJOINT
2
≥
TARGET
2
⇔
AVAILABLE
✓
The target is time-varying: raise it at rush hours, relax it at night.
Availability is a quantity the solver optimises, not directly a stored mass. All of it can be time-variant.

## Slide 36
V1
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
11 / 17
A booking enters
Three accepted bookings mark slots of the 12 h horizon
k (now)
prediction horizon, 72 steps, booked slots flagged
k + 72
V1
V2
V3
AT V1'S SLOT, K+8: 16 KG ASKED
T3₂ → T4
T3₄ → T4
T4
T3₁ → T3₃
T3₃ → T3₂
T3₄ → T3₂
Σ selected = booked flag · selected ≤ feasible
Only the selected pattern passes its per-tank masses
through
TANK STATE AT K+9, THE SAMPLE AFTER V1
next state = state + compression − reserved
·
T3₁
·
T3₂
·
T3₃
·
T3₄
·
T4
Horizon rolls: tanks moved,
selection re-optimised
,
commitments kept.
V1
V2
V3

## Slide 37
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
11 / 17
A booking enters
At V1's slot a pattern is required
k (now)
prediction horizon, 72 steps, booked slots flagged
k + 72
V1
V2
V3
AT V1'S SLOT, K+8: 16 KG ASKED
T3₂ → T4
T3₄ → T4
T4
T3₁ → T3₃
T3₃ → T3₂
T3₄ → T3₂
Σ selected = booked flag but selected ≤ feasible
Only the selected pattern passes its per-tank masses
through
TANK STATE AT K+9, THE SAMPLE AFTER V1
next state = state + compression − reserved
·
T3₁
·
T3₂
·
T3₃
·
T3₄
·
T4
Horizon rolls: tanks moved,
selection re-optimised
,
commitments kept.
V1
V2
V3
▲ observing V1

## Slide 38
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
11 / 17
A booking enters
Feasible patterns for V1: its mass on board, 16 kg asked
k (now)
prediction horizon, 72 steps, booked slots flagged
k + 72
V1
V2
V3
AT V1'S SLOT, K+8: 16 KG ASKED
T3₂ → T4
T3₄ → T4
T4
T3₁ → T3₃
T3₃ → T3₂
T3₄ → T3₂
Σ selected = booked flag BUT selected ≤ feasible
Only the selected pattern passes its per-tank masses
through
TANK STATE AT K+9, THE SAMPLE AFTER V1
next state = state + compression − reserved
·
T3₁
·
T3₂
·
T3₃
·
T3₄
·
T4
Horizon rolls: tanks moved,
selection re-optimised
,
commitments kept.
V1
V2
V3
▲ observing V1

## Slide 39
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
11 / 17
A booking enters
Exactly one pattern is selected
k (now)
prediction horizon, 72 steps, booked slots flagged
k + 72
V1
V2
V3
AT V1'S SLOT, K+8: 16 KG ASKED
T3₂ → T4
T3₄ → T4
T4
T3₁ → T3₃
T3₃ → T3₂
T3₄ → T3₂
Σ selected = booked flag BUT selected ≤ feasible
Only the selected pattern passes its per-tank masses
through
TANK STATE AT K+9, THE SAMPLE AFTER V1
next state = state + compression − reserved
·
T3₁
·
T3₂
·
T3₃
·
T3₄
·
T4
Horizon rolls: tanks moved,
selection re-optimised
,
commitments kept.
V1
V2
V3
▲ observing V1

## Slide 40
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
11 / 17
A booking enters
Its per-tank masses are subtracted from the next state
k (now)
prediction horizon, 72 steps, booked slots flagged
k + 72
V1
+1
V2
V3
AT V1'S SLOT, K+8: 16 KG ASKED
T3₂ → T4
T3₄ → T4
T4
T3₁ → T3₃
T3₃ → T3₂
T3₄ → T3₂
Σ selected = booked flag BUT selected ≤ feasible
Only the selected pattern passes its per-tank masses
through
TANK STATE AT K+9, THE SAMPLE AFTER V1
next state = state + compression − reserved
·
T3₁
−4.4 kg
T3₂
·
T3₃
·
T3₄
−6.0 kg
T4
Horizon rolls: tanks moved,
selection re-optimised
,
commitments kept.
V1
V2
V3
▲ observing past V1

## Slide 41
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
11 / 17
A booking enters
Horizon rolls: same commitments, new selection
k + 1 (10 min later)
prediction horizon, 72 steps, booked slots flagged
k + 72
+1
+1
V2
V3
AT V1'S SLOT, NOW K+7: SELECTION RE-OPTIMISED
T3₂ → T4
T3₄ → T4
T4
T3₁ → T3₃
T3₃ → T3₂
T3₄ → T3₂
Σ selected = booked flag BUT selected ≤ feasible
Only the selected pattern passes its per-tank masses
through
TANK STATE AT K+8, THE SAMPLE AFTER V1
next state = state + compression − reserved
·
T3₁
·
T3₂
·
T3₃
−5.2 kg
T3₄
−6.0 kg
T4
Horizon rolls: tanks moved,
selection re-optimised
,
commitments kept.
V1
V2
V3
▲ observing past V1

## Slide 42
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
12 / 17
A preliminary case
A short synthetic showcase, deterministic closed loop
6 h
winter afternoon, PV fading before the
arrivals
3
bookings placed while PV is up, arrivals after dark
Client
Request
Lead
Arrival
V1
16 kg
210 min
18:00
V2
14 kg
210 min
18:30
V3
18 kg
190 min
19:30

## Slide 43
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
13 / 17
Reserved pattern along each booking
Steps s1 and s2 of the selected pattern at every supervisory decision, from request ◆ to arrival ▼
Multiple reassignments
the solver changes the reserved
pattern of each client
25 → 97 %
0
commitments broken while new
bookings arrived
T4 raised for V1, then rebuilt only to
54 % for V3

## Slide 44
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
14 / 17
Compression timed to PV and arrivals
Compressor duty (C1, C2, C3) against PV power; dashed lines mark the three arrivals
Compression
front-loaded
into the
last two PV hours.
Compressors
mostly off
in the dark;
no eager refilling of emptied tanks.
A short burst ends
just before
each
arrival, moving just the mass of the
reserved pattern.

## Slide 45
CONTEXT
PROPOSAL
AVAILABILITY
BOOKINGS
RESULTS
CONCLUSIONS
16 / 17
Conclusions
THIS PAPER
Bookings enter as
hard constraints
, tank by tank.
One
reserved pattern
per client, with a tunable
safety margin.
Re-decided every ten minutes:
3 of 3
served on time,
compression inside the PV window.
TO ANSWER THE RESEARCH QUESTION
Benchmark against rule-based operation.
More scenarios, longer runs.
Disjoint availability target effect on KPIs.
Model mismatch from real operation.

## Slide 46
17 / 17
Thank you
Questions
European Fuel Cells and Hydrogen | Piero Lunghi Conference 2026 | Capri
Pol Cardona | IRI, CSIC-UPC
CSIC/I-LINK2025/ILINK25160 · SEAMLESS PID2023-148840OB-I00